## Slide 1: SAR -> Grafana
Chop chop

## Slide 2: SAR -> json
For inserting into elasticsearch having data in json is paramount
sadf an utility that does exactly that
If number of sample in sar file is big generated json are huge (50MB)
To keep it at an acceptable size ~5MB max sar data need to be splittted by time period based on number of sample
Split.sh is doing that, taking as input sar file it defines total number of samples and generate json file. (note json is in compacted form)
File name format <nodeID>_YYY-MM-DD_HH:MM:SS.json

## Slide 3: Json -> elasticsearch
2 components, filebeat and logstash
Filebeat monitor a directory for any new file, read it with almost no other processing that letting logstash known that file is a json object
Logstash take this object and start processing it
  Split json on a per sample basis
  Send each sample to pipeline (net, enet, disk and rest) for processing
  Each pipeline create a elasticsearch document and timestamp it correctly
Use of pipeline is needed to keep memory usage acceptable

## Slide 4: Logstash pipeline
Intake pipeline
Input filebeat
Filter split per sample
Output
net
disk
Net pipeline
Input Pipeline
move net to root
Delete all but net
Split net per nic
Output elastic
search
Disk pipeline
Input Pipeline
move disk to root
Delete all but disk
Split net per disk id
Output elastic
search

## Slide 5: Logstash pipeline 2
Intake pipeline
Net pipeline
Disk pipeline
Enet pipline
elasticsearch
Filebeat
Logstash

## Slide 6: Grafana queries from elasticsearch
Use of templating variable and variable of variable
For number of node can be huge creating a podid variable that is used to shorten compute# selectable is desirable.
  {"find": "terms", "field": "host.name.keyword"} filtered by /.*?[0-9](.*?[0-9]).*/ return a list of podid. Ex: snni2, ttrp1 etc
  {"find": "terms", "field": "host.name.keyword"} filtered by /${pod_id:regex}.*/ return list of compute based on $pod_id variable ex: UHN7cvmv{001..089}
  Appending :regex to pod_id variable is needed when multiple pod are selected, to insure that the multi selection is regex compatible

## Slide 7: Grafana graphing sar, smart and practical 
Lucene query
  To make graphs configurable by drop down, lucene query will use template variable. Appending :lucene to variable same as :regex to be lucene compatible
  net-dev.iface.keyword:${nic:lucene} AND host.name.keyword:${hostname:lucene}
  Graph will generate curve based on value from drop down variable
Metric
  Average net-dev.rxkB, average for sar data is average over last period of time
Grouping
  First by Terms: net-dev.iface.keyword
  Second by Terms: host.name.keyword
  Third by Date Histogram: @timestamp